### Changing to the Alternate IP address for the Instrument LAN Card

The default IP address for the Instrument LAN card is 198.168.0.1. Use the following procedure to change it to the alternate address.

- Open Windows Explorer, then double click on C:\Program Files\WatersInstruments\Waters DHCP Server Configuration.exe

- Select Server > Configuration Wizard.

- Highlight the Instrument LAN, and then click Next.

- Select the Alternate IP address 172.16.0.1.

- Click Next, then click Finish to complete the wizard.

- In the Waters DHCP Server Configuration page, select each component then click Remove.

- Click OK to close the Waters DHCP Server Configuration page.

- Reboot the host PC and allow it to complete initializing.

- Reboot the Acquity components, if applicable.

- Reboot the epc.

- Open MassLynx.